## Slide 1
TIAGO ROBOT
TIAGo Robot Simulation in ROS 2
Environment Setup, Gazebo Worlds, Autonomous Navigation, and MoveIt 2
SIMULATION DEMONSTRATION
ROS 2 Humble | October 2026
PAL Robotics public TIAGo simulation stack

## Slide 2
01 · ENVIRONMENT
Validated Simulation Environment
A reproducible ROS 2 stack running on a Windows workstation through WSL2.
HOST PLATFORM
Windows + WSL2
LINUX DISTRIBUTION
Ubuntu 22.04.5 LTS · x86_64
ROBOTICS MIDDLEWARE
ROS 2 Humble · Cyclone DDS
SIMULATOR
Gazebo Classic · WSLg / D3D12
ROBOT STACK
PAL TIAGo public simulation humble-devel
TOOLS
RViz2 · Nav2 · MoveIt 2 ros2_control
Nav2 / MoveIt 2
TIAGo ROS 2 Packages
ROS 2 Humble + Cyclone DDS
Ubuntu 22.04 on WSL2
Windows Workstation
Public simulation — no physical robot required
TIAGo Robot Simulation
02

## Slide 3
02 · GAZEBO WORLDS
Multiple Simulation Environments
The same TIAGo software stack was launched in three structurally different worlds.
Hospital
Long corridors and an irregular floor plan
WORLD 1
Factory
Large connected areas with multiple regions
WORLD 2
PAL Office
Dense rooms, doors, and narrow passages
WORLD 3
World selection changes geometry while preserving the robot, controllers, and ROS 2 interfaces.
TIAGo Robot Simulation
03

## Slide 4
03 · NAVIGATION
Nav2 Goal Selection in RViz2
The target pose is selected in RViz2; Nav2 converts it into motion commands for the simulated base.
RVIZ2 INTERFACE
Visible information
• 2D occupancy map of the office environment
• Inflated cost regions around walls and obstacles
• Live laser measurements around the robot
• Nav2 Goal tool for defining position and orientation
Nav2 Goal
TIAGo Robot Simulation
04
NAV2 GOAL

## Slide 5
03 · NAVIGATION
Navigation Execution in Gazebo
The video shows the physical execution result after a navigation target was issued.
12 s VIDEO
Observed result
• Starts from rest
• Moves smoothly through the office corridor
• Turns toward the right-side passage
• Stops near the requested destination
Click the video to play
Scope: point-to-point navigation execution; the planning interface is shown on the previous slide.
TIAGo Robot Simulation
05

## Slide 6
04 · MOVEIT 2
Interactive Arm Planning in RViz2
MoveIt 2 uses the current robot state and an interactive end-effector target to generate a joint trajectory.
MOTION PLANNING
Workflow
1
Select the arm planning group
2
Set the goal pose with the 6-DoF marker
3
Generate a collision-aware trajectory
4
Execute through ros2_control
Demo scope: free-space arm motion
TIAGo Robot Simulation
06

## Slide 7
04 · MOVEIT 2
Planned Arm Trajectory Execution
The generated trajectory is executed by the simulated TIAGo arm in Gazebo.
6 s VIDEO
Observed result
• Right arm moves from a folded pose to a forward extension
• Shoulder, elbow, and wrist move smoothly
• Base and torso remain stationary
• Trajectory completes without visible discontinuity
Click the video to play
Scope: free-space trajectory execution; no grasping or object interaction is shown.
TIAGo Robot Simulation
07

## Slide 8
SUMMARY
Demonstrated Capabilities
The public simulation stack is ready for repeatable TIAGo experiments without access to the physical robot.
01
Environment
ROS 2 Humble and the TIAGo public stack were installed and validated in WSL2.
02
Worlds
The robot was launched successfully in Hospital, Factory, and PAL Office environments.
03
Navigation
A target pose was selected in RViz2 and executed as point-to-point motion in Gazebo.
04
Manipulation
MoveIt 2 planned and executed a smooth right-arm trajectory in simulation.
Next steps
SLAM mapping · custom environments · object-aware manipulation · validation on the physical TIAGo
TIAGo Robot Simulation
08